## Slide 1: Erçin DİNÇER
Temel Bilgisayar Ağ Teknolojileri

## Slide 2: Günlük Hayatımızda Bilgisayar Ağları
Wireless
Kablolu Network
3G/4G-4.5G
DNS Ayarları

## Slide 3: IP Adresi

## Slide 4: IP Adresi
A Sinifi Adresler : 1.0.0.0 – 126.255.255.255 (00000001-01111111)
B Sinifi Adresler : 128.0.0.0 – 191.255.255.255 (10000000-10111111)
C Sinifi Adresler : 192.0.0.0 – 223.255.255.255 (11000000-11011111)
D Sinifi Adresler : 224.0.0.0 – 239.255.255.255 (11100000-11101111)
E Sinifi Adresler : 240.0.0.0 – 254.255.255.255 (11110000-11110111)
• 10.0.0.0 – 10.255.255.255 • 172.16.0.0 – 172.31.255.255 • 192.168.0.0 – 192.168.255.255

## Slide 5: IP Adresi
192.168.0.0 255.255.255.0 networkunu 2 alt ağa ayıralım.
11111111.11111111.11111111.00000000 : 255.255.255.0 (Şuanli subnet mask)
11111111.11111111.11111111.10000000: 255.255.255.128 (Yeni subnet mask)
192.168.0.0/24′ ü 6 alt subnete bölelim.
11111111.11111111.11111111.00000000 : 255.255.255.0 (Şuanli subnet mask) 11111111.11111111.11111111.11100000: 255.255.255.224 (Yeni subnet mask)

## Slide 6: OSI Referans Modeli

## Slide 7: Temel Kavramlar
Network Diagram
Network Tipleri (WAN, LAN, Peer to Peer)
  Fiber Kablolar
  Switch ve Hub Teknolojileri
  Server
  Topoloji Tipleri (Star, Bus, Ring)
  Firewall
  Routers
  Wireless Network
  Internet

## Slide 8: Network Diyagramı
The Internet
Other LANS
Firewall
Router
Fiber Optic Network Cable
Server
PC
Wireless Network
Wired Network
Switch
Notes: I wanted to present this diagram to help the viewer visually understand how a computer network was set-up. I linked each component to the same text links throughout the project.

## Slide 9
PEER TO PEER
WIDE AREA
LOCAL AREA
Notes: I used this slide as a Introduction to the different types of networks. I tried to let the graphics do the talking on this slide. I elaborated more on each network type on subsequent slides.

## Slide 10: Fiber Kablo
Reduces interference in the network
Transmit data faster than copper network cable
Allows for more bandwidth
Smaller and more fragile than copper cable
Standard Network Copper Cable
Notes: I felt this fiber optic cable graphic was a great graphic in that it, not only showed the fiber optic glass cables but, the colors fit in well with my project. I also wanted to show a small picture of a traditional wire cable just to contrast the two.

## Slide 11: Switch ve Hub
Network Switch
Network Hub
Notes: I used the same principle with switches and hubs as I did with the fiber optic cable in that I tried to contrast the newer component (switches) with the older ones (hubs). They two are hard to differentiate and look very similar but, I tried to outline the components below.

## Slide 12: Server
Notes: I used the same principle with switches and hubs as I did with the fiber optic cable in that I tried to contrast the newer component (switches) with the older ones (hubs). They two are hard to differentiate and look very similar but, I tried to outline the components below.

## Slide 13: Server
Notes: I used the same principle with switches and hubs as I did with the fiber optic cable in that I tried to contrast the newer component (switches) with the older ones (hubs). They two are hard to differentiate and look very similar but, I tried to outline the components below.

## Slide 14: Network Topolojileri
Star
Ring
Bus
Notes: I used the same principle with switches and hubs as I did with the fiber optic cable in that I tried to contrast the newer component (switches) with the older ones (hubs). They two are hard to differentiate and look very similar but, I tried to outline the components below.

## Slide 15: Firewall
Notes: I used the same principle with switches and hubs as I did with the fiber optic cable in that I tried to contrast the newer component (switches) with the older ones (hubs). They two are hard to differentiate and look very similar but, I tried to outline the components below.

## Slide 16: Router
Notes: I used the same principle with switches and hubs as I did with the fiber optic cable in that I tried to contrast the newer component (switches) with the older ones (hubs). They two are hard to differentiate and look very similar but, I tried to outline the components below.

## Slide 17: İnternet
Notes: I used the same principle with switches and hubs as I did with the fiber optic cable in that I tried to contrast the newer component (switches) with the older ones (hubs). They two are hard to differentiate and look very similar but, I tried to outline the components below.

## Slide 18: Title
Body text 1st layer
  Body text 2nd layer
    Body text 3rd layer
      Body text 4th layer
        Body text 5th layer